## Slide 1: NeuroDOT
Tutorial:
Pad File Generation

## Slide 2
Pad File Tutorial Overview
What is a pad file?
  NeuroDOT representation of the imaging system
  Optode array positions
  Measurement list: all information about each measurement for a given array design
Where are pad files used?
  One of three key components for generating a light model
  Anywhere a measurement list is needed
    Preprocessing
    Postprocessing
    Visualization
What will this tutorial will teach you
  The necessary inputs for building a pad file, and how to build it
  How to visualize a pad file in 2D and 3D
  How to adjust a pad file so the measurement list matches what is in the data

## Slide 3
NeuroDOT Set-Up – Output Directory
Once you’ve set your path, the next thing you should do is set your output directory.
  The output directory must be located within your path
  If it isn’t already in your path, you must add it to your path
You can set your own path to an output directory in the line shown above
An output directory specifies the location where files will be saved
  MATLAB, by default, will save files to the current directory
The following line of code will change your current directory to the output directory that you just specified 
Now you can save outputs directly to your output directory
Full example code section 
Example output directory

## Slide 4: Diffuse Optical Tomography
In diffuse optical tomography (DOT), arrays of optical sources and detectors are used to perform functional neuroimaging experiments on task-based or resting state modes of human brain function.
Analyses are broken into several pipelines:
  B: modeling of the tissue shape, optical property distribution, and source/detector locations
  C: modeling of the light emission, diffusion, and detection through the head
  D: preprocessing of the raw source-detector measurements
  E: reconstruction and spectroscopy of the preprocessed data and light model into a functional neuroimaging volume
  F: post-processing analysis of these results.

## Slide 5: Generating a Pad File
This tutorial will follow the Generating_a_pad_file_tutorial.m Matlab file which can be found in the Documentation/Scripts folder.
The tutorial will:
  Create an array of sources and detectors based a set of NeuroDOT sample data
  Populate an info structure with measurement information
  Visualize and double check aspects of the pad file to validate
  Demonstrate optional steps that may be necessary during pad file generation

## Slide 6
Running the script – Author’s Note
How the author runs the script
  Highlight and execute each section of code
    Ex: highlight lines 24-26  right click  hit “Evaluate Selection”
Alternate way of running the script
  For each section (beige) hit ctrl+enter
Note: DO NOT HIT THE GREEN “RUN” BUTTON to run this script
MATLAB versions to use
  Optimal version: MATLAB 2020b
Example
section

## Slide 7: What information goes into a pad file?
The Pad file for a given grid design contains a structure variable info that contains the spatial and topological information for the array as follows:
  info.optodes
    Structure containing spatial coordinates for sources and detectors in array
    info.optodes.spos2 – 2D coordinates of each sources
    info.optodes.spos3 – 3D coordinates of each source
    info.optodes.dpos2 – 2D coordinates of each detector
    info.optodes.dpos3 – 3D coordinates of each detector
  info.pairs
    Structure containing topological information for each source-detector measurement pair
    Each row of the subfields in info.pairs corresponds to a measurement and must be in the same order as the optical data for valid processing
    Generally, full list of sources and detectors is repeated for each wavelength/lambda.
    info.pairs.Src – source in measurement
    info.pairs.Det – detector in measurement
    info.pairs.NN – Nearest Neighbor class in array (e.g., info.pairs.NN=1 means this measurement is one of the closest in the grid design)
    info.pairs.WL – wavelength index of measurement
    info.pairs.lambda – actual wavelength of measurement (e.g., info.pairs.lambda=750 is a 750 nm measurement)
    info.pairs.Mod – Modulation type of measurement (e.g., ‘CW’, or, ‘FD’)
    info.pairs.r2d – 2D source-detector distances
    info.pairs.r3d – 3D source-detector distances

## Slide 8: Load nirs data and create grid
First, we’ll need to populate a grid with 2D and 3D optode locations
  3D optode locations are mandatory, the pad file cannot be created without these
  2D optode locations are ideal, but not necessary to generate the pad file
NeuroDOT is compatible with various raw data file formats including *.mat (shown in this tutorial), *.snirf, and *.nirs.
The PowerPoint “Tutorial_for_Loading_Raw_Data” and corresponding script “Script_for_Loading_Raw_Data” provide details on how to load raw data in these formats.
%% Load data and get optode locations
% Load data that contains optode locations and wavelengths
Data = load('NeuroDOT/Data/NeuroDOT_Data_Sample_CCW1');
% Create grid structure and place optode locations inside
% grid structure should contain the following fields at a minimum
% 3D source positions: grid.spos3
% 3D detector positions: grid.dpos3
grid = struct;
grid.spos3 = Data.info.optodes.spos3;
grid.dpos3 = Data.info.optodes.dpos3;
% If available, place 2D optode positions in grid structure
grid.spos2 = Data.info.optodes.spos2;
grid.dpos2 = Data.info.optodes.dpos2;

## Slide 9: Create info structure, visualize layout in 2D
%% Create info structure (this is the pad file)
params.lambda = unique(Data.info.pairs.lambda); %Ex: [750, 850]
params.mod = 'CW'; %Modulation type or frequency
params.CapName = 'ND_tutorial_pad'; %Create this yourself
info = Generate_pad_from_grid (grid,params);
%% Visualize pad file
% 2D layout - PlotCap (sources in red, detectors in blue)
PlotCap(info)
First, set parameters for pad file generation
  Lambda: wavelengths used by the nirs/DOT system
  Mod: modulation type or frequency
    Can be a string or frequency in Hz
  Cap name: name for the nirs/DOT system used in data collection
After that, visualize the pad in 2D and 3D

## Slide 10: Visualize layout in 3D
% 3D layout - PlotCap
params_cap.dimension = '3D';
PlotCap(info, params_cap);view([-40,30])
% 3D layout – Draw_Foci (sources in red, detectors in blue)
tpos=cat(1,info.optodes.spos3,info.optodes.dpos3); %SD positions
Ns=size(info.optodes.spos3,1); %Number of sources
Nd=size(info.optodes.dpos3,1); %Number of detectors
paramsFoci.color=cat(1,repmat([1,0,0],Ns,1),repmat([0,0,1],Nd,1));
paramsFoci.color(1,:) = [1 0.4 0.6]; %Pink for s1
paramsFoci.color(Ns+1,:) = [0.3010, 0.7450, 0.9330]; %Light blue for d1
figure;Draw_Foci_191203(tpos,paramsFoci);view([-40,30])
To use PlotCap for 3D visualizations set:
  params.dimension = ‘3D’
  Dimension defaults to 2D unless otherwise specified
Can also use Draw_Foci to visualize optode positions
  Array of all SD positions organized as: [source pos; detector pos]
  RGB array for all optodes: sources in red, detectors in blue
  Optional: setting the color of S1 and D1 to a lighter version of the SD colors
Draw_Foci
PlotCap

## Slide 11: Sanity checks, then save
%% Make sanity check plots
% Visualize r2d by itself (hist)
figure;histogram(info.pairs.r2d,1000);xlabel('R_S_D');...
ylabel('N_m_e_a_s');title('2D SD Separations');xlim([0 60])
% Visualize r3d by itself (hist)
figure;histogram(info.pairs.r3d,1000);xlabel('R_S_D');...
ylabel('N_m_e_a_s');title('3D SD Separations');xlim([0 60])
% Visualize r3d by NN (scatter)
figure;scatter(info.pairs.r3d,info.pairs.NN);xlabel('R3d');ylabel('NN');
title([info.optodes.CapName, ', 3D SD sep by NN'], 'interpreter', 'none');
%% Save pad file
save(['Pad_', info.optodes.CapName, '.mat'], 'info')
Check the source detector separations via histogram
  Only looking at measurements with a separations <= 60 mm
Make sure that nearest neighbors increase monotonically as a function of source detector separation: bottom

## Slide 12: Cropping measurement list to match data (1) Overview
NeuroDOT generates an info.pairs structure containing all possible measurements with
  Monotonically increasing sources within monotonically increasing detectors
Some data use only a subset of the total measurements
  Only NN’s 1, 2, 3, 4 and 5
  Only measurement pairs with a SD separation <= 30mm
Some data is ordered differently than we do in NeuroDOT
  Monotonically increasing detectors within monotonically increasing sources
The next 3 slides will serve as a mini tutorial for cropping info.pairs to match the measurements in the data
  Load in a neuroDOT data sample (NeuroDOT_Data_Sample_GV1) that uses a subset of the full measurement list
  Generate a pad file from optode positions given within the data file
    This will make a full pad file that will need to be trimmed down to match the measurement list in the data
  Adjust the newly made pad file to match the measurements seen in the data

## Slide 13: Cropping measurement list to match data (2) Generate Pad
%% Load data file
Data = load('NeuroDOT/Data/NeuroDOT_Data_Sample_GV1');
%% Generate and visualize pad file
% Optode positions
grid = struct;
grid.spos3 = Data.info.optodes.spos3;
grid.dpos3 = Data.info.optodes.dpos3;
grid.spos2 = Data.info.optodes.spos2;
grid.dpos2 = Data.info.optodes.dpos2;
% Params
params.lambda = unique(Data.info.pairs.lambda); % Ex: [750, 850]
params.mod = 'CW'; % Modulation type or frequency
params.CapName = 'ND_tutorial_pad_cropSection'; % Create this yourself
% Generate
info = Generate_pad_from_grid(grid,params);
% Visualize 2D
PlotCap(info)
Load the data and generate the pad file
Then, visualize the pad in 2D

## Slide 14: Cropping measurement list to match data (3) Get measurement lists
%% Get Measurement lists from Pad and from Data
% Create temp pairs structure, this will get modified to match data
temp = info.pairs;
% Make measurement list from pad
pad_measList_before = [temp.Src, temp.Det, temp.WL];
% Make measurement list from data
data_measList = [Data.info.pairs.Src, Data.info.pairs.Det,...
Data.info.pairs.WL];
% Are measurement lists in the same order?
order_before = isequal(Data.MeasList, pad_measList_before)
Next, create a temporary structure that’s a copy of info.pairs
  We’ll crop this structure, then place it back in the pad file
Make measurement lists from the pad and the data
Measurement lists contain the following info for each pair:
  Source number, Detector number, Wavelength
We’ll also check if the measurement lists are identical
  They shouldn’t be at this point
Data
Pad

## Slide 15: Cropping measurement list to match data (4) Crop pad
%% Crop to match data
% Get order of measurements in data
[~,Idx]=ismember(Data.MeasList,pad_measList_before,'rows');
% Re-order pairs structure
temp.r3d=[temp.r3d(Idx)];
temp.r2d=[temp.r2d(Idx)];
% temp.r2d = temp.r3d; %for sparse pads, uncomment this line - set r2d = to r3d
temp.NN = [temp.NN(Idx)];
temp.Src = [temp.Src(Idx)];
temp.Det = [temp.Det(Idx)];
temp.WL = [temp.WL(Idx);]; %Get correct size
temp.lambda = [temp.lambda(Idx)]; %Get corect size
temp.Mod = [temp.Mod(Idx,:),];
% Make sure measurements are identical
pad_measList_after = [temp.Src, temp.Det, temp.WL];
order_after = isequal(Data.MeasList, pad_measList_after)
% Sanity Check
% Visualize r3d by itself (hist)
figure;histogram(temp.r3d,1000);xlabel('R_S_D');ylabel('N_m_e_a_s');
title('SD Separations (Matched2Data)');xlim([0 60])
Now, get the correct order and measurements for the cropped pad and reorder the temp pairs structure
Validate that both measurement lists are identical and perform a final sanity check

## Slide 16: Cropping measurement list to match data (4) Save the cropped pad
%% Replace info.pairs with temp pairs and save pad file matched to data
info.pairs = temp;
save(['Pad_' info.optodes.CapName, '_matched2Data' '.mat'], 'info')
Finally, replace info.pairs with the cropped temp pairs structure
Then save your pad file

## Slide 17: Appendix: Explaining NN’s
Nearest Neighbors (NN’s) are an ordinal classification denoting how close a Source-Detector (SD) pair are to each other
  NN’s are stored within info.pairs.NN
NN’s can be used to threshold the data
  i.e. only use measurements from NN1’s, 2’s, etc.
Top right: NN’s organized by SD separation distance
Bottom : example NN classifications on 2D layout

## Slide 18: Appendix: Visualizing 2D layout in EEG style
% Load NIRx fullHead pad used in sparse pad light modeling tutorials
padname='FullHead_32x32';
load(['Pad_',padname,'.mat']);
% Turn eeg_style on and visualize
params_cap.eeg_style = 1;
PlotCap(info, params_cap)
Some arrays from commercial companies, such as NIRx utilize an EEG style layout for their 2D visualizations
NeuroDOT is equipped to visualize arrays in both EEG style and grid style
Set params.eeg_style = 1 when using PlotCap to visualize the 2D layout
  params.eeg_style defaults to 0 in PlotCap

## Slide 19: Help Expand NeuroDOT’s Utility!
Please fill out the NeuroDOT registration form to help us better develop the NeuroDOT toolbox and expand its utility to address your fNIRS/DOT data analysis needs:
  https://forms.gle/8QNGnx7ZbKuUHg3bA
Additionally, please provide specific feedback, or ask questions to the development team:
  https://forms.gle/jv6RkX5s784LgQC89
Note: you will not be contacted by the NeuroDOT development team unless you opt-in to receiving communications.

## Slide 20: That’s It (For Now)
Congratulations! You have finished the NeuroDOT Tutorial for Pad File Generation. Continue on to the NeuroDOT_Tutorial_Generating_a_Light_Model_Pad_24x28_With_AlignMe next to build the corresponding light model with your pad file.
See other Sample Results Appendices for example visualizations of these same processing steps on the other Sample Data included in the toolbox.
Also, see the PreProcessing and Reconstruction tutorials to gain a deeper understanding of the effects of altering the processing parameters.
NeuroDOT Support: neurodot-support@wustl.edu